## Slide 1: Inventory of consumables
Food
Water
Oxygen
Per day and for entire length of stay
Factor in back up in case of emergency?

## Slide 2: Food
Men
2500 calories per day
1260000 for entire duration
Woman
2000 calories per day
1008000 for entire duration
For a crew of 10 (5 men & 5 woman)
22500 calories per day
11340000 for entire duration

## Slide 3: Food cont…
Would the calorific requirement the same as on earth?
How will the nutritional guidelines be met?
ISS resupply mission every 90 days with less crew members on board.
Therefore is it possible to assume it is unfeasible for the resupply mission to carry all the food and food generation is needed?

## Slide 4: Water consumption
17472 L drinking water required for the 10 member crew. However the following will need to be taken into account:
Shower
Toilet flush
Oral and hand hygiene
Laundry
Food preparation
Water recovery will be crutial!

## Slide 5: Oxygen consumption
Low Activity metabolic load - 0.78 kg/day
Normal Activity metabolic load – 0.84 kg/day
High Activity metabolic load – 0.96 kg/day
5th Percentile nominal female – 0.52 kg/day
95th Percentile nominal male – 1.11 kg/day
423360 kg/per 18 months stay for 10 crew members
1 kg carbon dioxide produced per day
O2/N2 regulator needed

## Slide 7: An introduction to mars
Gravity on mars is roughly 38 % that on earth. g = 3.73 m/s²
Orbital period of 1.88 years
Mean pressure at surface is 0.60 kPa
The atmosphere on Mars consists of 95% carbon dioxide, 3% nitrogen, 1.6% argon and contains traces of oxygen and water
Mean temperature :−63 °C low: -87 °C high: 20 °C
43% amount of sunlight the earth receives. Roughly 430 W/m²
Surface is mainly hematite, dust is an issue for solar panels
planet has little heat transfer across its surface, poor insulation against assault of the solar wind and not enough atmospheric pressure to retain water in a liquid state. Mars is totally geologically dead; the end of volcanic activity has seemingly stopped the recycling of chemicals and minerals between the surface and interior of the planet.

## Slide 9: Aspects to be conserved
Water
Air
Food
Biomass
Waste
Thermal Energy

## Slide 10: Water
Water will cost £1M / litre to ship to station
Used for practically everything
Technology is already developed for water recycling so should be easy to implement.
Maintained in the same form and does not degrade.
In theoretically water could be completely conserved

## Slide 11: Air
Air consists of 79%N2 21%O2 and trace CO2
O2 used in respiration and CO2 produced.
Q. Can assume nitrogen is just a buffer gas and neither used or created.
Recycle CO2 back into O2
Trace contaminants need to be monitored/removed.
Humidity and temperature regulation.

## Slide 12: Food
Food is source of energy.
Converted into other forms, eg heat/work/body mass therefore cannot be conserved.
Will have to be supplied every 18months.
There is potential for some recycling of food waste/human waste.
Food could be created in the form of vegetables but would only be able to supplement the main food source.
As water is conserved, dehydrated foods may prove to be more practical than first thought.

## Slide 13: Biomass
Provides salad crop to supplement diet
Dietary nutrients gained from salad crop are relatively minor
Main benefit is the psychological advantage that would not be gained from prepared foods
Potential to use solid waste as fertilizer for food production, but would require prior treatment.

## Slide 14: Waste
Urine – Can be recycled to recovery water.
Food/human waste – Water could be extracted from solid waste. Dehydrated solids waste/food waste used for fertiliser.
Material Waste – More difficult to handle. Includes spent and damaged equipment. E.g. Water filters, clothing, broken machinery.

## Slide 15: Thermal Energy
Although assuming an unlimited energy source, it is considered good practise to minimise losses.
This would allow for future expansion of the station without requiring additional energy sources.
Thermal regulation of the station would be required to provide an acceptable working environment.
Losses would occur through all walls due to large temperature gradient. Could be minimised using insulation.
Potential for heat recovery using heat exchangers.

## Slide 16
Ref. Advanced Life Support Research and Technology Development Metric – Fiscal Year 2005 (Anthony J. Hanford, Ph.D.)

## Slide 17: Questions
Can we assume space is not a design issue, and could therefore use alternative technologies to in spaceships/submarines
Do you know anything about the conservation of methane.
Account for the function of the station? e.g. science experiments, extra-vehicular-activities.
Can we assume nitrogen is just a buffer gas and not created/destroyed.
Can we assume that the initial space requirement for equipment transport is not an issue.

## Slide 19: Presence and Nature of Water
Water very expensive to transport - worth investigation into how to access and utilise local water.
Water is not abundant in liquid and gaseous states.
  Due to the average atmospheric temperature and pressure being too low.
Ice is abundant at the poles and exists in ice sheets at lower latitudes (needs drilling to reach).

## Slide 20: Atmospheric Composition
Major Gases Present:
  Carbon Dioxide (CO2) - 95.32%
  Nitrogen (N2) - 2.7%
  Argon (Ar) - 1.6%
  Oxygen (O2) - 0.13%
  Carbon Monoxide (CO) - 0.08%
  Water Vapour (H2O) – 0.03%
http://nssdc.gsfc.nasa.gov/planetary/factsheet/marsfact.html

## Slide 21: Utilisation of CO2
Can utilise high levels of CO2 to produce water and oxygen using any of the following methods:
  Sabatier Reaction : CO2 + 4H2  CH4 + 2H2O
  Reverse Water Gas Shift Reaction : CO2 + H2  CO + H2O
  Combination : 3CO2 + 6H2  CH4 + 2CO + 4H2O
H2O can be electrolysed to produce O2 and H2 (which can be recycled back into the process).
  2H2O  2H2 + O2
Hydrogen is very light and therefore cheaper to transport. Oxygen and carbon elements found in situ.
In Situ Resource Utilisation (ISRU) http://isru.msfc.nasa.gov/